## Slide 1
MassDOER × TPS FELLOWSHIP PROJECT · APRIL 2026
Next-Generation
BESS Siting Tool
Selecting 231 Beacham St, Everett & 283 Eastern Ave, Chelsea
as Massachusetts’ Top Battery Energy Storage Investment Sites
Monzia Moodie, Regulatory & Policy Systems Analyst
Kadir Farah, Storage Systems & Development Specialist
Advisor: Marcus Anum | Sponsor: Ledum Nordee | Coach: Tyler Holloway
5,000 MW
2030 MA Storage Goal
119/125
Everett Tool Score
113/125
Chelsea Tool Score
$169M
Combined Gross CAPEX (Model)

## Slide 2
THE MASSACHUSETTS ENERGY STORAGE IMPERATIVE
Massachusetts Storage Gap at a Glance
INSTALLED + PIPELINE (STATEWIDE)
2,000+ MW
~40% of 5,000 MW target (including pipeline)
PERMITTED — SUFFOLK + MIDDLESEX
1,285 MW
~25% of target — concentrated in highest-value nodes
2030 STATUTORY MANDATE
5,000 MW
By July 31, 2030 · Chapter 239
The buildout gap is not a technology or capital problem — it is driven by siting, interconnection, and execution challenges.
⚡ 5,000 MW by July 31, 2030
Massachusetts’ statutory mandate — the most aggressive state storage target in the US (MA 2024 Climate Act, Chapter 239)
📉 ~ 2,000+ MW in operation or active development
~2+ GW of storage installed or in development (~40% of 5,000 MW target, including pipeline). Significant gap remains, requiring rapid and accurate site identification.
🏙 Suffolk + Middlesex Lead
1,285 MW permitted in two counties = 25.7% of the statewide 2030 goal — from the highest-grid-value zones in New England.
💰 $10B in Ratepayer Savings
Governor Healey’s 10X10X10 Executive Order ties storage deployment to $10 billion in projected customer savings by 2035.
Sources: MA 2024 Climate Act Chapter 239 (signed Nov 2024) · Mass.gov ESI Goals & Storage Target · Governor Healey 10X10X10 Executive Order (Mar 2026) · pv magazine USA (Dec 2025)

## Slide 3
THE PROBLEM: WHY BESS PROJECTS FAIL BEFORE THEY START
Developer Failure Modes
Sites are selected before EJ screening — triggering costly late-stage redesigns
Battery systems are sized without setback or zoning clarity
Revenue modeled without ISO-NE zone-specific LMP variability
Communities bear environmental burden with no structured benefit pathway
Interconnection costs estimated without hosting capacity data
What Our Tool Solves
EJ & CIA screening embedded before any site is shortlisted
MW sizing logic integrates grid hosting capacity as binding constraint
ISO-NE NEMA zone LMP, FCM, CPS, and SMART modeled in revenue stack
Community benefits layer: energy burden, health data, HCA templates
Eversource & National Grid hosting capacity data integrated by circuit
→

## Slide 4
METHODOLOGY FOUNDATION: BUILDING ON THE WORCESTER COUNTY MCE FRAMEWORK
Worcester County MCE Baseline (2025)
Criteria:
3 factors: roads, transmission lines, population density
Scoring:
Uniform equal weighting (33.3% each)
EJ Integration:
Population density as proxy — not EJ-specific
Revenue Model:
Not included
Legal/Zoning:
Not included
Suitability Classes:
5 classes (Very Low → Very High)
High + Very High:
40.25% of Worcester parcels identified
Limitation:
Single-county; no community layer; no legal framework
→
Enhanced
for S+M
Suffolk + Middlesex: Five-Layer MCE (2026)
Criteria:
5 independent scored dimensions (EJ, Grid, Zoning, Physical, Revenue)
Scoring:
Custom-weighted per regulatory priority; max 125 pts composite
EJ Integration:
OEJE MassGIS EJ data; CIA 33-indicator framework; energy burden
Revenue Model:
ISO-NE LMP, FCM SENE zone, CPS, SMART adder, ITC stacking
Legal/Zoning:
DOER Model Bylaw tiers, EFSB jurisdiction, Dover Amendment
Community Layer:
Energy burden, health rates, host community agreement benchmarks
Output:
13 municipalities ranked; 3 user audiences served simultaneously
Validated:
Top 2 scores → parcel-specific analysis confirmed by financial models
Sources: Worcester County Battery Storage Suitability Report (MCE/QGIS, 2025) · Worcester EV Charging Siting Analysis (2025) · Worcester Solar MCE Report (2025)

## Slide 5
THE BESS SITING TOOL: FIVE INTEGRATED EVALUATION LAYERS
Each layer scores 0–25 points · Maximum composite score: 125 · All 13 municipalities screened simultaneously across three user audiences
01
Environmental Justice & Regulatory Compliance
MassGIS OEJE 2020 EJ Population data · CIA 33-indicator framework (eff. July 2024) · Energy burden · Health burden (asthma, PM2.5) · CIA Standards 980 CMR 15.00 (Jan 2026)
All 13 municipalities EJ-designated · Chelsea & Everett: 100% EJ block group coverage · CIA compliance embedded pre-selection
02
Grid Feasibility & Hosting Capacity
Eversource Hosting Capacity Map / envelio Navigator · National Grid MA SDP · U.S. DOE Atlas · ORNL OpenEnergyHub · ISO-NE interconnection queue
KEY INSIGHT: Grid hosting capacity is the BINDING MW constraint — not parcel size. Everett feeder: 15 MW ceiling. Chelsea substation: 100 MW. Layer 2 drives the financial model.
03
Zoning, Permitting & Legal Framework
DOER Model Bylaw tiers (Oct 2025) · EFSB sole jurisdiction ≥10 MWh (July 2026) · MA Zoning Atlas · Municipal codes · Dover Amendment precedent
Both sites: I-1/I-2 Industrial (50 ft setback). Chelsea 400 MWh qualifies for EFSB sole jurisdiction path. Everett 60 MWh = local permitting path. Zero moratoriums.
04
Physical Feasibility & Site Characteristics
Industrial/brownfield parcels · Net buildable area after setbacks · MW sizing logic (interconnection-constrained, not land-constrained) · Brownfield bonus (energy community ITC)
231 Beacham: 15 MW / 60 MWh (4hr, feeder-constrained, $25.1M gross CAPEX) · 283 Eastern: 100 MW / 400 MWh (4hr, substation-scale, $144M gross CAPEX)
05
Revenue Modeling & Market Economics
ISO-NE NEMA zone LMP ($42.09/MWh DA 2024) · FCM SENE zone (FCA 18: $3.58/kW-mo) · Clean Peak Energy Certificates · SMART 3.0 adder · Federal ITC 40% (PWA + domestic content)
$130/kW-yr base revenue confirmed by models. Everett: −$2.2M NPV, 5.9% IRR (needs >$150/kW-yr). Chelsea: +$5.4M NPV, 8.8% IRR. 40% ITC confirmed; domestic content risk limits higher tiers.
Sources: MassGIS OEJE EJ Populations (2020) · Eversource Hosting Capacity Map · National Grid MA SDP · ISO-NE Market Reports · DOER Model Bylaw (Oct 2025) · BESS Financial Models — 231 Beacham (Everett) & 283 Eastern (Chelsea) · NREL ATB 2024

## Slide 6
HOW THE TOOL WORKS: DATA ARCHITECTURE & USER PATHWAYS
MassDOER Policy Staff
Pre-screen 83E procurement bids
Track 2030 goal progress live
Validate CIA compliance before approval
Connect to MassEnviroScreen (in dev.)
Private Developers
Score sites before acquisition
Model 2hr / 4hr / 8hr duration revenue
Stack ITC: base 30% → up to 40%+
Identify brownfield sites near substations
Community Stakeholders
View energy burden by neighborhood
Access CIA trigger flags
Track host community agreement values
Exercise independent CIA review rights
PRIMARY DATA SOURCES INTEGRATED INTO THE TOOL
ISO-NE isoexpress
LMP zone data, FCA results, load forecasts
iso-ne.com
Eversource Hosting Map
Circuit-level BESS hosting capacity, DER costs
eversource.com
National Grid SDP
Middlesex County feeder-level hosting capacity
nationalgridus.com
U.S. DOE Atlas
National hosting capacity benchmarks & links
energy.gov/cmei
MassGIS OEJE 2020
EJ block group designations, CIA indicators
mass.gov/massgis
NREL ATB 2025
Installed cost projections — validated by financial models
nrel.gov
DOER Model Bylaw
3-tier BESS zoning framework (Oct 2025)
mass.gov/doer
MA Zoning Atlas
Municipal industrial/commercial zoning
zoningatlas.org/ma
BESS Financial Models
Site-specific screening models — Everett & Chelsea
Project documents
Data compiled April 2026 · All sources publicly accessible · BESS financial screening models added as primary source for parcel-specific capacity and CAPEX validation

## Slide 7
LAYER 1: ENVIRONMENTAL JUSTICE SCREENING — MANDATORY MARCH 2026
⚖️ Massachusetts CIA Requirement (Effective March 2026): All new BESS in EJ communities must complete a 33-indicator Cumulative Impact Analysis covering pollution burden, health outcomes, and socioeconomic factors before state permitting. Massachusetts became the first state to mandate CIA for clean energy infrastructure (Chapter 8, Acts of 2021; OEJE CIA Standards Jan 23, 2026).
MA EJ Designation Criteria (OEJE)
Criterion 1:
Minority population ≥ 40% of census block group
Criterion 2:
Median HH income ≤ 65% of statewide median (~$54,850)
Criterion 3:
≥ 25% of households lack English proficiency
Criterion 4:
Minorities ≥ 25% AND municipal median income ≤ 150% statewide
Data source:
MassGIS 2020 EJ Population Layer (Census 2020 + ACS 5-yr)
EJ Coverage — Key Study Municipalities
Chelsea
Suffolk
100%
8.1%
2× state avg
East Boston
Suffolk
100%
9.2%
2× state avg
Everett
Middlesex
100%
7.8%
High
Malden
Middlesex
100%
6.1%
Elevated
Lowell
Middlesex
96%
7.4%
High
Cambridge
Middlesex
95%
4.8%
Average
Framingham
Middlesex
87%
5.6%
Elevated
Municipality
County
% EJ
E. Burden
Asthma
Sources: MassGIS 2020 EJ Population Layer · Mass.gov CIA · OEJE CIA Standards (Jan 2026) · MA Household Economic Burden Index (Dec 2022) · MA DPH Health Data

## Slide 8
LAYERS 2 & 3: GRID FEASIBILITY, HOSTING CAPACITY & ZONING FRAMEWORK
Grid Feasibility & Hosting Capacity
Eversource (Suffolk + most Middlesex)
envelio Grid Connection Navigator — parcel-level hosting capacity, seasonal data. Circuit-level limits are the binding MW constraint at urban BESS sites.
National Grid SDP (Lowell, Framingham)
CymeDist/EPRI DRIVE feeder-level analysis. FERC-approved Wholesale Distribution Tariff (Mar 2024): $20.94/mo + $0.51/kW demand.
DOE Atlas (national benchmark)
U.S. distribution hosting capacity atlas — 58 utilities, 26 states. MA required hosting maps since Nov 2019.
ORNL OpenEnergyHub
Bulk downloadable Eversource Eastern MA DG hosting capacity — enables programmatic analysis.
Interconnect Cost Reference (confirmed)
Everett 231 Beacham: $2.0M (feeder-scale). Chelsea 283 Eastern: $12.0M (substation upgrade). Confirmed by project financial models.
ISO-NE Queue (Jan 2026)
~14,000 MW total; 46% battery storage. 21 of 26 Cluster Study projects are battery storage — majority in Massachusetts.
Zoning, Permitting & Legal Framework
DOER Model BESS Bylaw — 3 Tiers (Oct 6, 2025):
Tier
Capacity
Industrial
Commercial
Residential
1
< 250 kWh
By-Right
By-Right
By-Right
2
250 kWh–10 MWh
By-Right
Site Plan
Spec. Permit
3
10–100 MWh
Site Plan
Spec. Permit
Spec. Permit
≥100 MWh
≥100 MWh
EFSB Sole
EFSB Sole
EFSB Sole
EFSB Sole Jurisdiction (July 1, 2026)
15-month consolidated permit for ≥100 MWh. Chelsea (400 MWh) qualifies. Everett (60 MWh) uses local permitting path. Both sites clear.
Dover Amendment (M.G.L. c.40A §3)
Upheld in Duxbury Energy Storage v. Duxbury ZBA (MA Land Court, Jun 2025). Standalone BESS protected.
AGO Moratorium Record
Every MA municipal BESS moratorium rejected. Zero moratoriums in Suffolk or Middlesex — both project sites in clear-permitting jurisdictions.
Sources: Eversource Hosting Capacity Map · National Grid MA SDP · U.S. DOE Atlas (Jul 2025) · DOER Model Bylaw (Oct 2025) · BESS Financial Models — confirmed interconnection costs

## Slide 9
LAYERS 4 & 5: PHYSICAL FEASIBILITY & REVENUE MODELING
Chart: 4hr BESS Revenue Stack — NEMA Zone ($/kW-yr)
| Arbitrage | FCM Capacity | Clean Peak CPS | Ancillary Svcs | SMART Adder
Low ($/kW-yr) | 40 | 31 | 15 | 2 | 10
High ($/kW-yr) | 80 | 48 | 65 | 10 | 25
ISO-NE NEMA Zone — Confirmed Revenue Basis
Both financial models use $130/kW-yr base · NEMA DA 2024 avg: $42.09/MWh · NEMA Summer 2025: $53.31/MWh · Scarcity Jun 24, 2025: ~$1,600/MWh · Capacity (FCA 18): $3.58/kW-mo · Sensitivity threshold: Everett needs >$150/kW-yr for positive NPV
MW Sizing is Interconnection-Constrained
Project scale is set by grid hosting capacity, NOT parcel size. 231 Beacham, Everett: 15 MW / 60 MWh (4hr) — feeder-level circuit connection at $2.0M. 283 Eastern, Chelsea: 100 MW / 400 MWh (4hr) — substation upgrade at $12.0M. Both confirmed by project financial models. Layer 2 is the binding MW ceiling.
NREL Cost Benchmarks — Model-Validated
Everett model: $300/kWh → Battery CAPEX $18M. Chelsea model: $280/kWh (scale discount at 400 MWh) → Battery CAPEX $112M. O&M: 2.0% of gross CAPEX/yr (both models). Augmentation at Year 10: 15% of battery CAPEX.
ITC at 40% — Domestic Content Risk Limits Higher Tiers
Both models assume 40% ITC: PWA (30%) + Domestic Content bonus (+10%). Low-income community and energy community bonuses (+10–20%) carry execution risk due to FEOC sourcing rules. Use 40% as base; model 50% as upside scenario only.
Investment Conditions
Everett: Negative NPV at $130/kW-yr; requires Section 83E contracts or CPS optimization to exceed $150/kW-yr threshold. Chelsea: Positive NPV (+$5.4M), conditionally viable; leverage of 50–65% at 5.5–7.5% interest rate can push equity IRR to 12–15% — requires contracted revenue.
Sources: BESS Financial Models (Everett 231 Beacham & Chelsea 283 Eastern, April 2026) · NREL 2025 Battery Storage Cost Projections (DOI 10.2172/2583471) · ISO-NE 2024 Annual Markets Report · OBBBA Jul 2025 Section 48E

## Slide 10
APPLYING THE TOOL: COMPOSITE SITING SCORES — ALL 13 MUNICIPALITIES
Five-layer MCE scores correctly identify Everett and Chelsea as top sites. Financial model analysis confirms their investment priority — though at different scales and with different investment conditions.
Everett
119
→ PROJECT SITE
Chelsea
113
→ PROJECT SITE
Lowell
105
East Boston
104
Malden
101
Framingham
96
Boston
91
Revere
93
Cambridge
84
Waltham
85
Somerville
81
Medford
81
Winthrop
56
Score dimensions: EJ (/25) + Grid (/25) + Zoning (/25) + Physical (/25) + Revenue (/25) = Max 125 composite · Note: Chelsea (113) is the stronger near-term investment. Everett (119) is the highest-scoring site at feeder scale (15 MW).
Sources: TPS BESS Siting Tool MCE analysis (April 2026) · BESS Financial Models — Everett 231 Beacham & Chelsea 283 Eastern · ISO-NE Market Data · DOER Model Bylaw

## Slide 11
HOW THE TOOL CHOSE: SUFFOLK vs. MIDDLESEX — COUNTY & SITE COMPARISON
Financial models confirm the tool’s top-two selections. Note key finding: Chelsea is the LARGER, more viable investment; Everett is the highest-scoring but smaller, feeder-scale project.
SUFFOLK COUNTY
4 municipalities analyzed
MIDDLESEX COUNTY
9 municipalities analyzed
4
Cities
100%
EJ-Designated
SENE
ISO-NE Zone
Eversource
Utility
9
Cities
100%
EJ-Designated
SENE+
NEMA
ISO-NE
Eversource
+Nat.Grid
Utilities
SELECTED: 283 Eastern Ave, Chelsea · Score 113/125 · 100 MW / 400 MWh
SELECTED: 231 Beacham St, Everett · Score 119/125 · 15 MW / 60 MWh
✔ STRENGTHS
✔ STRENGTHS
Highest EJ urgency (25/25) — 8.1% energy burden, CIA Very High
Largest project in study: 100 MW / 400 MWh (4hr)
Only site with positive NPV (+$5.4M at $130/kW-yr, 8.84% IRR)
I-1 Industrial · 400 MWh qualifies for EFSB sole jurisdiction path
$86.4M net CAPEX at 40% ITC — institutional-scale investment
Highest composite score in study (119/125 = 95.2%)
Lowest CAPEX: $25.1M gross / $15.1M net at 40% ITC
Perfect Grid score (25/25) — 0.2 mi to Mystic 345 kV; Very Low risk
Lowest interconnection cost ($2.0M feeder) — de-risks entry
I-2 Heavy Industrial — strongest zoning protection in study area
⚠ $12M interconnection — primary gating risk · Merchant IRR 8.84% needs contracted revenue for 12–15% equity · Battery $112M = 78% of total CAPEX
⚠ NEGATIVE NPV (−$2.2M) at $130/kW-yr merchant revenue · IRR ~5.9% — requires >$150/kW-yr for viability · Feeder-scale (60 MWh) — local permit path only
Key insight: A high composite score does not automatically equal investable economics. Chelsea (113) is the stronger near-term investment. Everett (119) is the highest-quality site requiring contracted revenue to unlock viability.

## Slide 12
SITE SELECTION #1 — 231 BEACHAM STREET, EVERETT, MA · TOOL SCORE: 119/125 · 15 MW / 60 MWh
Five-Layer Composite Score
EJ & Regulatory
25/25
Grid Feasibility
25/25
Zoning & Permitting
22/25
Physical Feasibility
24/25
Revenue Potential
23/25
COMPOSITE TOTAL
119 / 125
Address:
231 Beacham Street, Everett, MA 02149
Zone / Use:
I-2 Heavy Industrial · Brownfield parcel
Grid Access:
0.2 mi to Eversource Mystic 345 kV substation
ISO-NE Zone:
SENE · Feeder-level connection ($2.0M interconnection)
Financial Model — Site Analysis (Model-Confirmed)
15 MW
Modeled Capacity (4hr · feeder-constrained)
60 MWh
Energy Storage (4-hour system)
$25.1M
Gross CAPEX ($18M battery + $2M IC + $3.1M other)
$15.1M
Net CAPEX after 40% ITC ($10.1M ITC value)
−$2.2M
NPV @ 8% WACC · IRR: 5.93% · Payback: 10.4 yrs
INVESTMENT VERDICT: CONDITIONALLY VIABLE — NOT STANDALONE INVESTABLE
At $130/kW-yr merchant revenue: negative NPV, 5.9% IRR. Requires Section 83E contracted revenue or CPS optimization above $150/kW-yr threshold. At 50% ITC + $150/kW-yr revenue: project turns viable. First-phase feeder project; scale expansion requires transmission interconnection study.
Sources: BESS Financial Model — 231 Beacham Street, Everett (April 2026) · MassGIS OEJE 2020 EJ Population Layer · Eversource Hosting Capacity Map · MA Household Economic Burden Index · DOER Model Bylaw (Oct 2025) · ISO-NE SENE Zone Data

## Slide 13
SITE SELECTION #2 — 283 EASTERN AVENUE, CHELSEA, MA · TOOL SCORE: 113/125 · 100 MW / 400 MWh
Five-Layer Composite Score
EJ & Regulatory
25/25
Grid Feasibility
23/25
Zoning & Permitting
20/25
Physical Feasibility
21/25
Revenue Potential
24/25
COMPOSITE TOTAL
113 / 125
Address:
283 Eastern Avenue, Chelsea, MA 02150
Zone / Use:
I-1/I-2 Industrial · Urban industrial parcel
Grid Access:
0.4 mi to Eversource Chelsea electrical substation
ISO-NE Zone:
SENE · Substation-scale connection ($12M interconnection)
Financial Model — Site Analysis (Model-Confirmed)
100 MW
Modeled Capacity (4hr · substation-scale)
400 MWh
Energy Storage (4-hour system)
$144M
Gross CAPEX ($112M battery + $12M IC + $20M other)
$86.4M
Net CAPEX after 40% ITC ($57.6M ITC value)
+$5.4M
NPV @ 8% WACC · IRR: 8.84% · Payback: 8.5 yrs
INVESTMENT VERDICT: CONDITIONALLY VIABLE — LEVERAGE UNLOCKS 12–15% EQUITY IRR
At $130/kW-yr: +$5.4M NPV, 8.84% IRR. Leverage (50–65% debt at 5.5–7.5%) pushes equity IRR to 12–15%. Requires contracted or partially hedged revenue. $12M interconnection is primary gating risk — cost escalation to >$20M approaches breakeven. Section 83E CPEC contract would confirm bankability.
Sources: BESS Financial Model — 283 Eastern Avenue, Chelsea (April 2026) · MassGIS OEJE 2020 EJ Population Layer · Eversource Hosting Capacity Map · MA Household Economic Burden Index · DOER Model Bylaw (Oct 2025) · ISO-NE SENE Zone Data

## Slide 14
FINANCIAL COMPARISON: MODEL-VALIDATED INVESTMENT PROFILES — EVERETT vs. CHELSEA
All figures drawn directly from project financial screening models (April 2026) · Revenue: $130/kW-yr · ITC: 40% (PWA + domestic content) · WACC: 8% unlevered
231 Beacham St, Everett
15 MW / 60 MWh · 4hr · Score 119/125
NOT INVESTABLE
merchant basis
Gross CAPEX
$25,130,000
ITC (40%)
−$10,052,000
Net CAPEX
$15,078,000
Year 1 Revenue
$1,950,000
Year 1 O&M (2%)
$502,600
Year 1 EBITDA
$1,447,400
NPV @ 8% WACC
−$2,198,134
Unlevered IRR
5.93%
Payback
10.4 years
Viability threshold: >$150/kW-yr revenue OR 50% ITC → NPV turns positive (+$2.3M at 50% ITC)
283 Eastern Ave, Chelsea
100 MW / 400 MWh · 4hr · Score 113/125
CONDITIONALLY
VIABLE
Gross CAPEX
$144,000,000
ITC (40%)
−$57,600,000
Net CAPEX
$86,400,000
Year 1 Revenue
$13,000,000
Year 1 O&M (2%)
$2,880,000
Year 1 EBITDA
$10,120,000
NPV @ 8% WACC
+$5,365,186
Unlevered IRR
8.84%
Payback
8.5 years
Leverage upside: 50–65% debt at 5.5–7.5% → equity IRR 12–15% · At 50% ITC: NPV rises to +$19.3M
Sources: BESS Financial Models — Everett 231 Beacham & Chelsea 283 Eastern (April 2026) · Sensitivity: battery cost vs. revenue IRR; interconnection vs. ITC NPV · Discount rate 8% unlevered · ITC 40% base case

## Slide 15
PROJECT-LEVEL ECONOMIC IMPACT: WHAT THE TOOL’S SITE SELECTIONS DELIVER
$169M
Combined Gross CAPEX (Both Sites)
$101.5M
Net CAPEX at 40% ITC (Combined)
115 MW
Combined Modeled Capacity
$11.6M/yr
Combined Year 1 EBITDA
5.9–8.8%
Unlevered IRR Range (Both Sites)
ITC at 40% — Execution Risk Limits Higher Tiers
Both models confirm 40% ITC: PWA (30%) + domestic content bonus (+10%). The model commentary explicitly notes that achieving domestic content requires compliance with evolving FEOC supply chain rules — execution risk exists. Energy community and low-income community bonuses (+10–20%) are possible upside but should be modeled as scenarios, not base cases. At 50% ITC, Chelsea NPV rises from +$5.4M to +$19.3M; Everett NPV moves from −$2.2M to +$2.3M.
Interconnection Cost: The Primary Gating Variable
Chelsea’s $12M interconnection is the dominant risk factor. Each $1M increase in interconnection cost reduces NPV by approximately $1.7M at 40% ITC. An escalation to $20M+ renders Chelsea near-breakeven at base revenue. Everett’s $2M feeder connection is low-risk but limits scale to 15 MW — confirming the tool’s Layer 2 (Grid Feasibility) as the binding constraint on project economics, not parcel area.
Revenue Certainty Is the Investment Condition
Neither site is investable on a purely merchant basis at $130/kW-yr. Everett produces negative NPV. Chelsea is marginally positive. The path to institutional-grade returns requires: (1) Section 83E CPEC contracts from the MA 2024 Climate Act, (2) CPS multiplier optimization (up to 25× at monthly system peak), or (3) partial revenue hedging via Forward Capacity Market contracts. The tool identifies these revenue mechanisms via Layer 5 — connecting site quality directly to market opportunity.
The Tool as Underwriter — A Refined Narrative
‘We built a tool to fix how BESS sites are selected — then tested it on Chelsea and Everett to show what is actually investable and why.’ The tool’s five-layer MCE scores of 119 and 113 correctly identified the two strongest sites in the study area. Financial model analysis refines the picture: Chelsea (113) is the more viable near-term investment at $144M gross CAPEX; Everett (119) is the highest-quality site requiring contracted revenue to unlock positive returns. This is the tool working as designed.
Sources: BESS Financial Models (April 2026) · ISO-NE 2024 Annual Markets Report · OBBBA Jul 2025 ITC Section 48E · MassCEC 2024 Annual Report · MA 2024 Climate Act Section 83E · MassDOER CPS ACP schedule

## Slide 16
THE TOOL’S UNIQUE ADVANTAGE: ASSESSING ANY CITY IN MASSACHUSETTS
Suffolk and Middlesex were chosen for their demographic, economic, and grid representativeness of Massachusetts. The five-layer MCE framework — validated by financial models for 231 Beacham St and 283 Eastern Ave — scales to every county.
Feature
Single-Factor Analysis
(Worcester MCE Baseline)
Five-Layer BESS Siting Tool
(Our Approach — Validated by Financial Models)
EJ Compliance
Population density proxy
OEJE block group designation + CIA 33 indicators + energy burden
Revenue Model
Not included
ISO-NE zone LMP + FCM + CPS + SMART adder + ITC (40% base, 50% upside)
Legal / Zoning
Not included
DOER Model Bylaw tiers + EFSB jurisdiction + Dover Amendment status
Audience Design
Single (technical)
Three simultaneous: MassDOER, developers, community stakeholders
Site Validation
Predictive only
MCE top scores validated by project financial models (Everett & Chelsea)
Scalability
Worcester County only
Any MA county — same data: MassGIS, ISO-NE, Eversource, National Grid
Statewide inference: The brownfield+substation siting pattern, NEMA/SENE LMP advantage, EJ overlay in urban MA, EFSB jurisdiction, and the five-layer MCE model all transfer to Worcester, Springfield, New Bedford, and every Massachusetts urban county. The financial model structure — interconnection-constrained MW sizing, 40% ITC base, $130/kW-yr revenue floor — applies directly. Suffolk and Middlesex were the validated proof of concept.
Sources: Worcester Battery Storage MCE Report (2025) · TPS BESS Siting Tool MCE Analysis (April 2026) · BESS Financial Models — Everett 231 Beacham & Chelsea 283 Eastern (April 2026)

## Slide 17
CONCLUSION: SITE-SPECIFIC FEASIBILITY — INTERCONNECTION, SCALE, AND THE MODEL-VALIDATED INVESTMENT CASE
“We built a tool to fix how BESS sites are selected — then tested it on Chelsea and Everett to show what is actually investable and why.”
Interconnection Findings
231 Beacham, Everett: $2.0M feeder connection — low risk, low cost, limits scale to 15 MW. Feeder-level circuit confirmed as binding MW constraint. Scale expansion requires transmission-level interconnection study with Eversource.
283 Eastern, Chelsea: $12.0M substation upgrade — high cost, high capacity. Model shows NPV drops ~$1.7M per $1M of additional interconnection. Cost certainty via utility pre-application study is prerequisite for investment decision.
Tool’s Layer 2 (Grid Feasibility) is the binding output for MW sizing — not parcel area. This is a critical finding: the tool works correctly, but financial modeling must follow hosting capacity data.
Both sites avoid the $1.9–9.5M/mile underground cable replacement that kills urban project economics. Confirmed by model’s actual interconnection cost assumptions.
Scale & Financial Findings
Everett: 15 MW / 60 MWh (4hr) · Gross CAPEX $25.1M · Net $15.1M · IRR 5.93% · NPV −$2.2M at $130/kW-yr. Becomes viable above $150/kW-yr or at 50% ITC. Lowest-barrier entry point in the study.
Chelsea: 100 MW / 400 MWh (4hr) · Gross CAPEX $144M · Net $86.4M · IRR 8.84% · NPV +$5.4M at $130/kW-yr. Leverage of 50–65% debt pushes equity IRR to 12–15%. Strongest investment case in study.
Chelsea (score 113) is the stronger near-term investment despite Everett’s higher composite score (119). A high MCE score identifies the best-quality sites — financial viability depends on scale, interconnection, and contracted revenue.
Both sites need Section 83E contracted CPEC revenue for investment-grade returns. This is the policy mechanism the MA 2024 Climate Act created — and the tool positions both sites to compete for it.
Next Steps
Submit interconnection pre-applications to Eversource for 231 Beacham (feeder study, $2M budget) and 283 Eastern (substation study, $12M budget) to confirm capacity headroom and cost range.
Initiate Section 83E Round 2 bid preparation for Chelsea 283 Eastern (~$130–$144M CAPEX, 100 MW / 400 MWh) — this is the primary path to contracted revenue that makes the project bankable.
Validate ITC qualification: engage tax equity counsel to confirm energy community (brownfield) and low-income community bonus eligibility at both sites. 50% ITC vs. 40% changes NPV by $2.3M (Everett) and $13.9M (Chelsea).
Expand financial model to Worcester County, Bristol County, and Hampden County using same interconnection-first MW sizing methodology. Tool’s five layers directly feed the financial model structure.
TPS × MassDOER Fellowship Project · April 2026 · Monzia Moodie & Kadir Farah · Advisor: Marcus Anum
Financial models: BESS_Financial_Model_Final__Everette_.xlsx · BESS_Financial_Model_Final__Chelsea_.xlsx

## Slide 18
THE BOTTOM LINE: FOUR TAKEAWAYS FOR THIS AUDIENCE
01
The tool works — and it selected the right sites.
Five-layer MCE scoring across 13 municipalities in two counties surfaced 231 Beacham St, Everett (119/125) and 283 Eastern Ave, Chelsea (113/125) as the top investment sites before a single dollar of project capital was committed. Financial model analysis confirmed both selections. The five-layer framework is replicable in any Massachusetts county using the same publicly available data sources.
02
Grid hosting capacity is the binding variable — not land.
The most important methodological finding: project scale at both sites is set by the circuit or substation interconnection capacity, not by parcel area. Everett: 15 MW (feeder-limited, $2M connection). Chelsea: 100 MW (substation-scale, $12M connection). This means the tool’s Layer 2 must precede Layer 4 in any siting workflow. Sites near high-capacity substations on brownfield parcels are the priority profile across the Commonwealth.
03
Chelsea is the stronger near-term investment. Everett needs contracted revenue.
A higher MCE score does not equal a better investment. Chelsea (score 113) produces a positive NPV of +$5.4M at base revenue assumptions with leverage upside to 12–15% equity IRR. Everett (score 119) produces a negative NPV of −$2.2M at the same revenue — it becomes viable only above $150/kW-yr or at 50% ITC. Both sites require Section 83E contracted CPEC revenue for institutional-grade returns.
04
The tool de-risks investment decisions that Massachusetts needs made now.
The 5,000 MW mandate requires approximately 85+ projects the size of Chelsea to be completed by July 2030. The tool compresses the siting timeline, embeds EJ compliance before site acquisition, surfaces interconnection cost risk before capital is deployed, and identifies the revenue mechanisms that make projects bankable. It is designed to generalize — this is the proof of concept.
TPS × MassDOER Fellowship Project · April 2026 · Monzia Moodie & Kadir Farah · Advisor: Marcus Anum

## Slide 19
Questions & Discussion
Monzia Moodie · Regulatory & Policy Systems Analyst
Kadir Farah · Storage Systems & Development Specialist
Advisor: Marcus Anum | Sponsor: Ledum Nordee | Coach: Tyler Holloway
Suggested discussion areas:
Interconnection pre-application strategy for 231 Beacham and 283 Eastern
Section 83E Round 2 bid positioning for the Chelsea 100 MW project
ITC qualification path: energy community + low-income community bonus eligibility
Expanding the five-layer MCE framework to Worcester, Bristol, and Hampden Counties
TPS × MassDOER Fellowship · April 2026